## Slide 1
Advanced Topic
1

## Slide 2
Outline
Why FPGA
  Introduction
  Development Flow
Optimize for FPGA
  Reports
  Loop optimization
  Memory Optimization
  Other techniques
2

## Slide 3: What are FPGAs?
“Field Programmable Gate Array” (FPGA)
“Gates” refers to transistors
  These are the tiny pieces of hardware on a chip that make up the design
“Array” means there are many of them manufactured on the chip
  Many = Billions
  They are arranged into larger structures as we will see
“Field Programmable” means the connections between the internal components are programmable after deployment
FPGA = Programmable Hardware
What is an FPGA?
First, let’s define the acronym. It’s a Field Programmable Gate Array.

## Slide 4: How to build Hardware Blocks?
Look-up Tables and Registers
Memory Block
20 Kb
addr
data_in
data_out
On-chip RAM Blocks
DSP Blocks
66
Custom 64-bit
Large logic
Larger
memories
Custom Math Functions
Small memories
Custom small logic
Then, It’s All Connected
Together
Blocks are connected with custom routing determined by your code

## Slide 5: How to Connect to Host?
Accelerated functions run on a PCIe attached FPGA card.
The host interface is also “baked in” to the FPGA design.
This portion of the design is pre-built and not dependent on your source code.

## Slide 6: Intel FPGA
Implementing Optimized Custom Compute Pipelines (CCPs) synthesized from compiled code
Pre-Compiled BSP
Memory Interface
Host Link
I/O
CCP
On-chip Memory
CCP
On-chip Memory
On-chip Memory
On-chip Memory
CCP CCP CCP
On-chip Memory
CCP
On-chip
Memory
Custom Compute Pipeline

## Slide 7: Pipeline
+
Load
Load
Store
Loop Control
for (int i=0; i<LIMIT; i++) {
c[i] = a[i] + b[i];
}
Data Path
Control Path
Hardware is added for
Computation
Memory Loads and Stores
Control and scheduling
– Loops & Conditionals
Connecting pipeline together
Handshaking signals for variable latency paths
Operations with a fixed latency
are clustered together
Fixed latency operations improve
  Area: no handshaking signals required
  Performance: no potential stalling due to variable latencies
a
b
c
d

## Slide 8: Simultaneous Independent Operations
The compiler automatically identifies independent operations
Simultaneous hardware is built to increase performance
This achieves data parallelism in a manner similar to a superscalar processor
Number of independent operations only bounded by the amount of hardware
c = a + b;
f = d * e;
+
c
a
b d
*
e
f

## Slide 9: On-Chip Memories Built for Kernel Scope Variables
//kernel scope cgh.single_task<>([=]() {
int arr[1024];
…
arr[i] = …; //store to memory
…
… = arr[j] //load from memory
…
} //end kernel scope
Pipeline
.
.
.
.
.
On-chip memory structure for array arr
32-bits
1024
Sto. re
.
.
Lo.ad
Custom on-chip memory structures are built for the variables declared with the kernel scope
Or, for memory accessors with a target of local
Load and store units to the on- chip memory will be built within the pipeline

## Slide 10: Pipeline Parallelism for Single Work-Item Kernels
handle.single_task<>([=]() {
… //accessor setup
for (int i=0; i<LIMIT; i++) {
c[i] += a[i] + b[i];
}
});
+
Load Load
Store
i=2
i=0
i=1
Single work-item kernels almost always contain an outer loop
Work executing in multiple stages of the pipeline is called “pipeline parallelism”
Pipelines from real-world code are normally hundreds of stages long
Your job is to keep the data flowing efficiently
+
Load
Load
Store
i=2
i=1
i=0
Key Concept
Custom built-in dependencies make FPGAs powerful for many algorithms
handle.single_task<>([=]() {
int b = 0;
for (int i=0; i<LIMIT; i++) { b += a[i];
}
});
Dependencies Within the Single
Work-Item Kernel
When a dependency in a single work-item kernel can be resolved by creating a path within the pipeline, the compiler will build that in.

## Slide 11: Data Parallelism
The most common technique is to unroll your loops
handle.single_task<>([=]() {
… //accessor setup
#pragma unroll
for (int i=1; i<3; i++) { c[i] += a[i] + b[i];
}
});
Stage 1
Stage 2
Stage 3
Time
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Iteration 3
Iteration 2
Iteration 1
The compiler will still pipeline an unrolled loop, combining the two techniques
– A fully unrolled loop will not be pipelined since all iterations will kick off at once
Unrolled Loops Still Get Pipelined
Stage 1
Stage 2
Stage 3
Time
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Iteration 3
Iteration 2
Iteration 1
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Iteration 6
Iteration 5
Iteration 4
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Iteration 9
Iteration 8
Iteration 7
handle.single_task<>([=]() {
… //accessor setup
#pragma unroll 3
for (int i=1; i<9; i++) { c[i] += a[i] + b[i];
}
});

## Slide 12: Task Parallelism?
FPGAs can run more than one kernel at a time
– The limit to how many independent kernels can run is the amount of resources available to build the kernels
Data can be passed between kernels using pipes
– Another great FPGA feature explained in the Intel® oneAPI DPC++ FPGA Optimization Guide
Kernels launched parallel_for() or parallel_for_work_group() with a NDRange/work-group size of >1
So, Can We Build These? NDRange Kernels
…//application scope
queue.submit([&](handler &cgh) {
auto A = A_buf.get_access<access::mode::read>(cgh); auto B = B_buf.get_access<access::mode::read>(cgh); auto C = C_buf.get_access<access::mode::write>(cgh);
cgh.parallel_for<class VectorAdd>(num_items, [=](id<1> wiID) { c[wiID] = a[wiID] + b[wiID];
});
});
…//application scope
Yes, no problem, and you will learn to code them!
But, tasks usually imply more optimal pipeline structures.
The loop optimizations are limited for NDRange kernels.

## Slide 13
Outline
13
Why FPGA
  Introduction
  Development Flow
Optimize for FPGA
  Reports
  Loop optimization
  Memory Optimization
  Other techniques

## Slide 14: Accelerate Direct Programming on FPGA
Optimized Code
Intel® VTune™ Profiler
or Profiler Reports
Intel® DPC++ Compatibility Tool
Existing CUDA code
New Code
Existing C++
Existing OpenCL™
Applications
Optimization Reports
Emulation
Data Parallel C++
Intel® FPGA SDK
for OpenCL™
Bitstream Compilation

## Slide 15: FPGA Development Flow with oneAPI
FPGA Emulator target (Emulation)
  Compiles in seconds
  Runs completely on the host
Optimization report generation
  Compiles in seconds to minutes
  Identify bottlenecks
FPGA bitstream compilation
  Compiles in hours
  Enable profiler to get runtime analysis
Long Compile!!
dpcpp –fintelfpga *.cpp/*.o [device link options] [-Xs arguments]
Language
DPCPP = Data Parallel C++
Target Platform
Input Files source or object
Link Options
FPGA-Specific
Arguments

## Slide 16: Emulation
Get it Functional
Does my code give me the correct answers?
Quickly generate x86 executables that represent the kernel
Debug support for
– Standard DPC++ syntax, channels, print statements
dpcpp -fintelfpga <source_file>.cpp –DFPGA_EMULATOR
dpcpp Compiler
./mycode.emu
… Running …
mycode.cpp
Declare the device_selector as type cl::sycl::intel::fpga_emulator
Include fpga_extensions.hpp
Include –DFPGA_EMULATOR in your compilation command
#include <CL/sycl/intel/fpga_extensions.hpp>
using namespace cl::sycl;
...
#ifdef FPGA_EMULATOR intel::fpga_emulator_selector device_selector;
#else
intel::fpga_selector device_selector; #endif
queue deviceQueue(device_selector);
...

## Slide 17: Compiling
A report showing optimization, area, and architectural information will be produced in <file_name>.prj/reports/
– We will discuss more about the report later
-fsycl-link
dpcpp -fintelfpga <file_name>.o -Xshardware
Two Step Method:
dpcpp -fintelfpga <source_file>.cpp -c -o <file_name>.o
One Step Method:
dpcpp -fintelfpga <source_file>.cpp -fsycl-link -Xshardware
The default value for –fsycl-link is -fsycl-link=early which produces an early image object file and report
The profiler will be instrumented within the image and you will be able to run the executable to return information to import into Intel® Vtune Amplifier.
To compile to FPGA executable without profiler, leave off –Xsprofile.
Two Step Method:
dpcpp -fintelfpga <source_file>.cpp -c -o <file_name>.o dpcpp -fintelfpga <file_name>.o –Xshardware -Xsprofile
One Step Method:
dpcpp -fintelfpga <source_file>.cpp –Xshardware -Xsprofile
Compile to FPGA Executable with Profiler Enabled
Compiling to Produce an Optimization Report

## Slide 18: Compiling
Compiling FPGA Device Separately and Linking
In the default case, the DPC++ Compiler handles generating the host executable, device image, and final executable
It is sometimes desirable to compile the host and device separately so changes in the host code do not trigger a long compile
host_only.cpp
has_kernel.cpp
Partition code
Then run this command to compile the FPGA image:
dpcpp -fintelfpga has_kernel.cpp –fsycl-link=image –o has_kernel.o –Xshardware
This command to produce an object file out of the host only code:
dpcpp -fintelfpga has_kernel.cpp –c –o host_only.o
This command to put the object files together into an executable:
dpcpp -fintelfpga has_kernel.o host_only.o –o a.out –Xshardware
This is the long
compile

## Slide 19
Outline
Why FPGA
  Introduction
  Development Flow
Optimize for FPGA
  Reports
  Loop optimization
  Memory Optimization
  Other techniques
19

## Slide 20: Reports
HTML Report
Static report showing optimization, area, and architectural information
Automatically generated with the object file
– Located in <file_name>.prj\reports\report.html
Dynamic reference information to original source code
Optimization Report – Throughput Analysis
Loops Analysis and Fmax II sections
Actionable feedback on pipeline status of loops
  Shows loop carried dependencies
and bottlenecks
  Especially important for single work- item kernels since they have an outer loop
Show estimated Fmax of each loop

## Slide 21: Reports
Optimization Report – Area Analysis
Generate detailed estimated area utilization report of kernel scope code
Detailed breakdown of resources by system blocks
Provides architectural details of HW
– Suggestions to resolve inefficiencies
The system view of the Graph Viewer shows following types of connections
  Control
  Memory, if your design has global or local memory
  Pipe, if your design uses pipes
Optimization Report – Graph Viewer

## Slide 22: Reports
Optimization Report – Schedule Viewer
Schedule in clock cycles for different blocks in your code
HTML Kernel Memory Viewer
Helps you identify data movement bottlenecks in your kernel design. Illustrates:
Memory replication
Banking
Implemented arbitration
Read/write capabilities of each memory port

## Slide 23: Profiler
Inserts counters and profiling logic into the HW design
Dynamically reports the performance of kernels
Enable using the – Xsprofile option with dpcpp
CCU
Load
Store
+
Load
Memory Mapped Registers
To Host
Collecting Profiling Data
Run the executable that integrates the kernel with the profiler using
A profile.json file will be produced
Import the profile.json file into the Intel® Vtune™ Profiler
aocl profile -s <path/to/source>.source /path/to/host-executable

## Slide 24
Outline
Why FPGA
  Introduction
  Development Flow
Optimize for FPGA
  Reports
  Loop optimization
  Memory Optimization
  Other techniques
24

## Slide 25: Types of Kernels (Review)
There are two types of kernels in Data Parallel C++
  Single work-item
  NDRange
For FPGAs, the compiler will automatically detect the kind of kernel input
Loop analysis will only be done for single work-item kernels
Most loop optimizations will only apply to single work-item kernels
Most optimized FPGA kernels are single work-item kernels
Single work items kernels are kernels that contain no reference to the work item ID.
Usually launched with the group handler member function single_task().
Or, launched with other functions and given a work-group/NDRange size of 1.
Almost always contain an outer loop.
Single Work-Item Kernels
…//application scope
queue.submit([&](handler &cgh) {
auto A = A_buf.get_access<access::mode::read>(cgh); auto B = B_buf.get_access<access::mode::read>(cgh); auto C = C_buf.get_access<access::mode::write>(cgh);
cgh.single_task<class swi_add>([=]() { for (unsigned i = 0; i < 128; i++) {
c[i] = a[i] + b[i];
}
});
});
…//application scope

## Slide 26: Understanding Initiation Interval
dpcpp will infer pipelined parallel execution across loop iterations
– Different stages of pipeline will ideally contain different loop iterations
Best case is that a new piece of data
enters the pipeline each clock cycle
c = a + b
load a
load b
1
1
store c
n
- Iteration number
…
cgh.single_task<class swi_add>([=]() { for (unsigned i = 0; i < 128; i++) {
c[i] = a[i] + b[i];
}
});
…
Serial execution is the worst case. One iteration needs to complete fully before a new piece of data enters the pipeline.
Worst Case Best Case
For Begin
For End
Op 2
Op 3
Op 1
Op 2
Op 3
Op 1
i0
i1
i2
i2
i2
i3
i0
i1

## Slide 27: In-Between Scenario
L = K
v
…
…
…
…
10
…
II = 6
6 cycles later, next iteration enter the loop body
Sometimes you must wait more than one clock cycle to input more data
Because dependencies can’t resolve fast enough
How long you have to wait is called
Initiation Interval or II
Total number of cycles to run kernel is about (loop iterations)*II
– (neglects initial latency)
Minimizing II is key to performance
Why Could This Happen?
Memory Dependency
– Kernel cannot retrieve data fast enough from memory
_accumulators[(THETAS*(rho+RHOS))+theta] += increment;
Value must be retrieved from global memory and incremented

## Slide 28: Use Local Memory
Transfer global memory contents to local memory before operating on the data
…
constexpr int N = 128; queue.submit([&](handler &cgh) {
auto A = A_buf.get_access<access::mode::read_write>(cgh);
cgh.single_task<class unoptimized>([=]() { for (unsigned i = 0; i < N; i++)
A[N-i] = A[i];
}
});
});
…
…
constexpr int N = 128; queue.submit([&](handler &cgh) {
auto A = A_buf.get_access<access::mode::read_write>(cgh);
cgh.single_task<class optimized>([=]() { int B[N];
for (unsigned i = 0; i < N; i++) B[i] = A[i];
for (unsigned i = 0; i < N; i++) B[N-i] = B[i];
for (unsigned i = 0; i < N; i++) A[i] = B[i];
});
});
…
Non-optimized
Optimized
What Can You Do? Tell the Compiler About Independence
#pragma ivdep
– Dependencies ignored for all accesses to memory arrays
#pragma ivdep array(array_name)
– Dependency ignored for only array_name accesses
#pragma ivdep array(A)
for (unsigned i = 1; i < N; i++) { A[i] = A[i – X[i]];
B[i] = B[i – Y[i]];
}
Dependency ignored for A array Dependency for B still enforced
#pragma ivdep
for (unsigned i = 1; i < N; i++) { A[i] = A[i – X[i]];
B[i] = B[i – Y[i]];
}
Dependency ignored for A and B array

## Slide 29: Solution
What Can You Do?
Do a simpler calculation
Pre-calculate some of the operations on the host
Use a simpler type
Use floating point optimizations (discussed later)
Increase the distance in pipeline stages between when the data enters the pipeline and you need to use it
– See the “Relax Loop-Carried Dependency” in the Optimization Guide for more information

## Slide 30: Loop Unrolling
How Else to Optimize a Loop?
Unoptimized loop
Sum of 4 values for every work-item
Store a new result every 4 iterations
(Note: loop unrolling can be applied to NDRange or single work-item kernels)
Store every 4 iterations
accum = 0;
for (size_t i=0; i<4; i++)
{
accum += data_in[(gid*4)+i];
}
sum_out[gid] = accum;
For Begin
For End
Store
Load
accum reg
+
The compiler will still pipeline an unrolled loop, combining the two techniques
– A fully unrolled loop will not be pipelined since all iterations will kick off at once
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Iteration 3
Iteration 2
Iteration 1
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Iteration 6
Iteration 5
Iteration 4
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
Iteration 9
Iteration 8
Iteration 7
handle.single_task<>([=]() {
… //accessor setup
#pragma unroll 3
for (int i=1; i<9; i++) { c[i] += a[i] + b[i];
}
});

## Slide 31: Fmax
The clock frequency the FPGA will be clocked at depends on what hardware your kernel compiles into
More complicated hardware cannot run as fast
The whole kernel will have one clock
The compiler’s heuristic is to sacrifice clock frequency to get a higher II
A slow operation can slow down your entire kernel by lowering the clock frequency
How Can You Tell This Is a Problem?
Fmax II report tells you the target frequency for each loop in your code.
cgh.single_task<example>([=]() { int res = N;
#pragma unroll 8
for (int i = 0; i < N; i++) { res += 1;
res ^= i;
}
acc_data[0] = res;
});

## Slide 32: Solution
Make the calculation simpler
Tell the compiler you’d like to change the trade off between II and Fmax
  Attribute placed on the line before the loop
  Set to a higher II than what the loop currently has
[[intelfpga::ii(n)]]
Area
The compiler sacrifices area in order to improve loop performance. What if you would like to save on the area in some parts of your design?
Give up II for less area
– Set the II higher than what compiler result is
Give up loop throughput for area
  Compiler increases loop concurrency to achieve greater throughput
  Set the max_concurrency value lower than what the compiler result is
[[intelfpga::ii(n)]]
[[intelfpga::max_concurrency(n)]]

## Slide 33
Outline
Why FPGA
  Introduction
  Development Flow
Optimize for FPGA
  Reports
  Loop optimization
  Memory Optimization
  Other techniques
33

## Slide 34: Memory Model
Private Memory
  On-chip memory, unique to work- item
Local Memory
  On-chip memory, shared within workgroup
Global/Constant Memory
    Visible to all workgroups
    On-chip cache for constant memory
Kernel
Global Memory
Constant Memory
it
rkgroup
Local Memory
Work- Work-
em item
Private Private
Memory Memory
WoWo
it
rkgroup
Local Memory
Work- Work-
em item
Private Private
Memory Memory
it
rkgroup
Local Memory
Work- Work-
em item
Private Private
Memory Memory
WoWorkgroup
Local Memory
Work- item
Private Memory
Work- item
Private Memory
Understanding Board Memory Resources
Memory Type
Physical Implementation
Latency (clock cycles)
Throughput (GB/s)
Capacity (MB)
Global
DDR
240
34.133
8000
Local
On-chip RAM
2
~8000
66
Private
On-chip RAM / Registers
2/1
~240
0.2
Key takeaway: many times the solution for a bottleneck caused by slow memory access will be to use local memory instead of global

## Slide 35: Global Memory
Is it Slow?
If the data is constant values, consider implementing it in a constant memory
Data will be transferred by the host to a global memory space and an on-chip memory space
On-chip memory space is visibile to all work items for NDRange kernels
auto a = a_buf.get_access<sycl::access::mode::read, sycl::access::target::constant_buffer>(cgh);
Add the constant_buffer access mode to the accessor constructor
We’ve seen this before... This will appear as a
memory dependency problem
Transfer global memory contents to local memory before operating on the data
…
constexpr int N = 128; queue.submit([&](handler &cgh) {
auto A = A_buf.get_access<access::mode::read_write>(cgh);
cgh.single_task<class unoptimized>([=]() { for (unsigned i = 0; i < N; i++)
A[N-i] = A[i];
}
});
});
…
…
constexpr int N = 128; queue.submit([&](handler &cgh) {
auto A = A_buf.get_access<access::mode::read_write>(cgh);
cgh.single_task<class optimized>([=]() { int B[N];
for (unsigned i = 0; i < N; i++) B[i] = A[i];
for (unsigned i = 0; i < N; i++) B[N-i] = B[i];
for (unsigned i = 0; i < N; i++) A[i] = B[i];
});
});
…
Non-optimized
Optimized

## Slide 36: Local Memory
Local Memory Considerations for Parallel Kernels
Declaring a variable in the kernel scope creates a private memory space
– Always works with single work-item kernels because there’s just 1
work item
Visibility between work-items is a concern in parallel kernels
2 ways to create local memory that work-items in a work- group can share
Within your kernel scope when using the parallel_for_work_group handler member function to launch the kernel
By creating an accessor with the access::target::local target
No buffer argument because host cannot access it
No way to size the memory, it will be
the default size of 16kB always
Creating Local Memory for NDRange Kernels
cgh.parallel_for_work_group<class myKernel>(
range<1>(8), range<1>(8), [=](group<1> myGroup)
{
//Code for work-group
//This variable is shared between work-items
//This variable can be sized int myLocal[8];
…
accessor <int, 1,
sycl::access::mode::read_write, sycl::access::target::local> local_mem(sycl::range<1>(wgroup_size), cgh);

## Slide 37: Local Memory Bottlenecks
If more load and store points want to access the local memory than there are ports available, arbiters will be added
These can stall, so are a potential bottleneck
Show up in red in the Memory Viewer section of the optimization report
Natively, the memory architecture has 2 ports
The compiler optimizes memory accesses to map to these without arbitration Your job is to write code the compiler can optimize
Local Memory Interconnect
M20K
M20K M20K M20K M20K M20K
Kernel Pipeline
port 0
port 1

## Slide 38: Memory Solutions
Double-Pumped Memory Example
Increase the clock rate to 2x
Compiler can automatically implement double- pumped memory – turning 2 ports to 4
//kernel scope
...
int array[1024];
array[ind1] = val; array[ind1+1] = val;
calc =
array[ind2]
+
array[ind2+1];
…
Local Memory Replication Example
//kernel scope
…
int array[1024]; int res = 0;
ST array[ind1] = val; #pragma unroll
for (int i = 0; i < 9; i++)
LD res += array[ind2+i];
calc = res;
…
Turn 4 ports of double-pumped memory to unlimited ports Drawbacks: logic resources, stores must go to each replication

## Slide 39: Memory Solutions
Coalescing
//kernel scope
…
local int array[1024]; int res = 0;
#pragma unroll
for (int i = 0; i < 4; i++)
array[ind1*4 + i] = val;
#pragma unroll
for (int i = 0; i < 4; i++)
res += array[ind2*4 + i];
calc = res;
…
Continuous addresses can be coalesced into wider accesses
Banking
s)
Divide the memory into independent fractional pieces (bank
//kernel scope
…
int array[1024][2];
array[ind1][0] = val1; array[ind2][1] = val2;
calc =
(array[ind2][0] +
array[ind1][1]);
…
Compiler looks at lower indices by default Indices for banking must be a power of 2 size

## Slide 40: Memory Optimization Attributes
Attribute | Usage
numbanks | [[intelfpga::numbanks(N)]]
bankwidth | [[intelfpga::bankwidth(N)]]
singlepump | [[intelfpga::singlepump]]
doublepump | [[intelfpga::doublepump]]
max_replicates | [[intelfpga::max_replicates(N)]]
simple_dual_port | [[intelfpga::simple_dual_port]]
Note: This is not a comprehensive list. Consult the Optimization Guide for more.

## Slide 41: Pipes
Pipes – Element the Need for Some Memory
Create custom direct point-to-point communication between CCPs with Pipes
CCP 1
CCP 2
CCP 3
Pipe
Pipe
Global Memory
Task Parallelism By Using Pipes
Launch separate kernels simultaneously Achieve synchronization and data sharing using pipes
Make better use of your hardware

## Slide 42
Outline
Why FPGA
  Introduction
  Development Flow
Optimize for FPGA
  Reports
  Loop optimization
  Memory Optimization
  Other techniques
42

## Slide 43: Other Optimization Techniques
Avoid Expensive Functions
Expensive functions take a lot of hardware and run slow
Examples
  Integer division and modulo (remainder) operators
  Most floating-point operations except addition, multiplication, absolution, and comparison
  Atomic functions
Inexpensive Functions
Use instead of expensive functions whenever possible
  Minimal effects on kernel performance
  Consumes minimal hardware
Examples
  Binary logic operations such as AND, NAND, OR, NOR, XOR, and XNOR
  Logical operations with one constant argument
  Shift by constant
  Integer multiplication and division by a constant that is to the power of 2
  Bit swapping (Endian adjustment)

## Slide 44: Other Optimization Techniques
Use Least-“Expensive” Data Type
Understand cost of each data type in latency and logic usage
  Logic usage may be > 4x for double vs. float operations
  Latency may be much larger for float and double operations compared to fixed point types
Measure or restrict the range and precision (if possible)
  Be familiar with the width, range and precision of data types
  Use half or single precision instead of double (default)
  Use fixed point instead of floating point
  Don’t use float if short is sufficient
Floating-Point Optimizations
Apply to half, float and double data types
Optimizations will cause small differences in floating-point results
  Not IEEE Standard for Floating-Point Arithmetic (IEEE 754-2008) compliant
Floating-point optimizations:
  Tree Balancing
  Reducing Rounding Operations

## Slide 45: Other Optimization Techniques
Tree-Balancing
Floating-point operations are not associative
  Rounding after each operation affects the outcome
– ie. ((a+b) + c) != (a+(b+c))
By default the compiler doesn’t reorder floating-point operations
  May creates an imbalance in a pipeline, costs latency and possibly area
Manually enable compiler to balance operations
  For example, create a tree of floating-point additions in SGEMM, rather than a chain
  Use -Xsfp-relaxed=true flag when calling dpcpp
Rounding Operations
For a series of floating-point operations, IEEE 754 require multiple rounding operation
Rounding can require significant amount of hardware resources
Fused floating-point operation
  Perform only one round at the end of the tree of the floating-point operations
  Other processor architectures support certain fused instructions such as fused multiply and accumulate (FMAC)
  Any combination of floating-point operators can be fused
Use dpcpp compiler switch -Xsfpc

## Slide 46: References and Resources
Website hub for using FPGAs with oneAPI
  https://software.intel.com/content/www/us/en/develop/tools/oneapi/components/fpga. html
Intel® oneAPI Programming Guide
  https://software.intel.com/content/www/us/en/develop/download/intel-oneapi- programming-guide.html
Intel® oneAPI DPC++ FPGA Optimization Guide
  https://software.intel.com/content/www/us/en/develop/download/oneapi-fpga- optimization-guide.html
FPGA Tutorials GitHub
  https://github.com/intel/BaseKit-code-samples/tree/master/FPGATutorials

## Slide 47
Thank you